Summary of IR Protocols to be Used for 3rd Party Remote Control Manufacturers

Report prepared by Jackson Gehman – January 17th, 2006

Edited by Bryce Fricke to include Maestro IR Fan Speed Controls – March 30th, 2007

The purpose of this document is to provide a quick summary of Lutron’s IR protocol as it relates to the information that 3rd-party remote control manufacturers will require in order to configure their software appropriately to meet Lutron’s standards of quality.

This document contains:

- Lutron’s infrared technical specifications

- Charts that identify the IR capability of the transmitters sold along with the dimming products.

- Charts that identify the IR codes that each Lutron dimming product utilizes

Lutron Infrared Technical Specifications:

# IR Carrier Frequency:			40.0 kHz

Duty Cycle:				40%

Single Bit Time:			2.288 milliseconds

Baud Rate:				437 bps

Command Length:			36 bits

Command Duration:			82.368 milliseconds

Logic One:				Presence of IR modulated at 40.0 kHz

Logic Zero:				Absence of IR

Transmit Order:			Transmit the most significant bit first

General Function:			IR code is transmitted while a button is held down

Timeout Function:	Timeouts may not occur until at least seven-seconds of continuous IR transmission has taken place.

Transmitter Functionality:

Spacer:

| Transmitter Model Number: | Available Addresses | Available Commands: |
| --- | --- | --- |
| SP-HT | All Lighting | This Lutron remote control is not compatible with other 3rd party remotes. |

Maestro IR:

| Transmitter Model Number: | Available Addresses: | Available Commands: |
| --- | --- | --- |
| MIR-ITFS | All Lighting | Full Off Lower Raise Favorite Scene Full On |

Maestro IR Fan/Light:

| Transmitter Model Number: | Available Addresses: | Available Commands: |
| --- | --- | --- |
| MIR-ITFS-LF | All Lighting All Fans | Full Off Lower Raise Favorite Scene Full On |

Maestro IR Fan:

| Transmitter Model Number: | Available Addresses: | Available Commands: |
| --- | --- | --- |
| MIR-ITFS-F | All Fans | Full Off Lower Raise Favorite Scene Full On |

Spacer System:

| Transmitter Model Number: | Available Addresses: | Available Commands: |
| --- | --- | --- |
| SPS-FSIT | All Lighting | Full Off Lower Raise Scene 1 |
| SPS-4IT | All Lighting | Full Off Lower Raise Scene 1 Scene 2 Scene 3 Scene 4 |
| SPS-5WC(R) (Not a hand-held remote control) Scene 5 behaves like a “full-on” | All Lighting | Full Off Lower Raise Scene 1 Scene 2 Scene 3 Scene 4 Scene 5 |

Grafik Eye & Radio RA:

| Transmitter Model Number: | Available Addresses: | Available Commands: |
| --- | --- | --- |
| GRX-IT | All Lighting | Full Off Lower Raise Scene 1 Scene 2 Scene 3 Scene 4 |
| GRX-8IT | All Lighting | Full Off Lower Raise Scene 1 Scene 2 Scene 3 Scene 4 Scene 5 Scene 6 Scene 7 Scene 8 |
| GRX-8IT Custom Scene 16 behaves like a “full-on” for Radio RA products. | All Lighting | Full Off Lower Raise Scene 9 Scene 10 Scene 11 Scene 12 Scene 13 Scene 14 Scene 15 Scene 16 |

PerSONNA and PerSONNA System:

| Transmitter Model Number: | Available Addresses: | Available Commands: |
| --- | --- | --- |
| PN-HT | All Lighting | This Lutron remote control is not compatible with other 3rd party remotes. |
| GRX-IT | All Lighting | Full Off Lower Raise Scene 1 Scene 2 Scene 3 Scene 4 |

Sivoia Shades:

| Transmitter Model Number: | Available Addresses: | Available Commands: |
| --- | --- | --- |
| SVQ-OCIT | All Shades | Close Open Lower Raise Programming Mode Set Limits Ind. Level Adjust Mode |
| SVQ-3PIT | All Shades | Close Open Preset 1 Preset 2 Preset 3 Lower Raise Programming Mode Set Limits Ind. Level Adjust Mode Preset Lock |
| SVQ-4GD-OCIT | All Shades All Shades in Zone 1 All Shades in Zone 2 All Shades in Zone 3 All Shades in Zone 4 All Front Shades Front Shades in Zone 1 Front Shades in Zone 2 Front Shades in Zone 3 Front Shades in Zone 4 All Rear Shades Rear Shades in Zone 1 Rear Shades in Zone 2 Rear Shades in Zone 3 Rear Shades in Zone 4 | Close Open Lower Raise Programming Mode Set Limits Ind. Level Adjust Mode |
| SVQ-4S2G-IT | All Shades All Front Shades All Rear Shades | Close Open Lower Raise Programming Mode Set Limits Ind. Level Adjust Mode |
|  | All Lighting | Full Off Scene 1 Scene 2 Scene 3 Scene 4 |

Product Specific IR Codes:

Maestro IR Lighting Codes:

| Transmitter Button: | IR Command: | Pronto Command: |
| --- | --- | --- |
| Full Off | FF88BD120h | 0000 0069 0007 0007 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 005a 00b4 005a 01c2 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 005a 00b4 005a 01c2 |
| Lower | FF8882140h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c |
| Raise | FF8882220h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 |
| Favorite Scene | FF8884B70h | 0000 0069 0007 0007 032a 010e 005a 010e 005a 0168 005a 00b4 005a 005a 00b4 005a 010e 0168 032a 010e 005a 010e 005a 0168 005a 00b4 005a 005a 00b4 005a 010e 0168 |
| Full On | FF8884B80h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 0168 005a 00b4 005a 005a 010e 0276 |

The only command that does not get repeated when a button is held down is the Full-On command.

Maestro IR Fan Codes:

| Transmitter Button: | IR Command: | Pronto Command: |
| --- | --- | --- |
| Full Off | FF887D140h | 0000 0069 0006 0006 0338 010B 005A 0164 01BD 005A 005A 010B 005A 005A 005A 0216 0338 010B 005A 0164 01BD 005A 005A 010B 005A 005A 005A 0216 |
| Lower | FF8842120h | 0000 0069 0006 0006 0338 010B 005A 0164 005A 0164 005A 0164 005A 00B4 005A 01BD 0338 010B 005A 0164 005A 0164 005A 0164 005A 00B4 005A 01BD |
| Raise | FF8842240h | 0000 0069 0006 0006 0338 010B 005A 0164 005A 0164 005A 010B 005A 00B4 005A 0216 0338 010B 005A 0164 005A 0164 005A 010B 005A 00B4 005A 0216 |
| Favorite Scene | FF8844B10h | 0000 0069 0007 0007 0338 010B 005A 0164 005A 010B 005A 00B4 005A 005A 00B4 010B 005A 0164 0338 010B 005A 0164 005A 010B 005A 00B4 005A 005A 00B4 010B 005A 0164 |
| Full On | FF8844BE0h | 0000 0069 0006 0000 0338 010B 005A 0164 005A 010B 005A 00B4 005A 005A 01BD 010B |

The only command that does not get repeated when a button is held down is the Full-On command.

Spacer System Codes:

| Transmitter Button: | IR Command: | Pronto Command: |
| --- | --- | --- |
| Full Off | FF88BD120h | 0000 0069 0007 0007 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 005a 00b4 005a 01c2 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 005a 00b4 005a 01c2 |
| Scene 1 | FF88BD1D0h | 0000 0069 0007 0007 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 010e 005a 005a 0168 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 010e 005a 005a 0168 |
| Scene 2 | FF88BD240h | 0000 0069 0007 0007 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 00b4 005a 021c 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 00b4 005a 021c |
| Scene 3 | FF88BD2B0h | 0000 0069 0008 0008 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 005a 005a 005a 00b4 0168 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 005a 005a 005a 00b4 0168 |
| Scene 4 | FF88BD710h | 0000 0069 0007 0007 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 010e 010e 005a 0168 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 010e 010e 005a 0168 |
| Scene 5 (Full On) | FF88BD7E0h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 021c 01c2 |
| Lower | FF8882140h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c |
| Raise | FF8882220h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 |

The only command that does not get repeated when a button is held down is the Scene-5 / Full-On command.

Grafik Eye Codes:

| Transmitter Button: | IR Command: | Pronto Command: |
| --- | --- | --- |
| Full Off | FF88BD120h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 005a 00b4 005a 01c2 |
| Scene 1 | FF88BD1D0h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 010e 005a 005a 0168 |
| Scene 2 | FF88BD240h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 00b4 005a 021c |
| Scene 3 | FF88BD2B0h | 0000 0069 0008 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 005a 005a 005a 00b4 0168 |
| Scene 4 | FF88BD710h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 010e 010e 005a 0168 |
| Scene 5 | FF88BD7E0h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 021c 01c2 |
| Scene 6 | FF88BD470h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 005a 010e 010e 0168 |
| Scene 7 | FF88BD480h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 005a 00b4 005a 0276 |
| Scene 8 | FF88BDD40h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 010e 005a 005a 005a 005a 021c |
| Scene 9 | FF88BDDB0h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 010e 005a 00b4 005a 00b4 0168 |
| Scene 10 | FF88BDE20h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 0168 010e 005a 01c2 |
| Scene 11 | FF88BDED0h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 0168 005a 00b4 005a 005a 0168 |
| Scene 12 | FF88BDB70h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 00b4 005a 00b4 005a 010e 0168 |
| Scene 13 | FF88BDB80h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 00b4 005a 010e 0276 |
| Scene 14 | FF88BD810h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 00b4 021c 005a 0168 |
| Scene 15 | FF88BD8E0h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 00b4 010e 010e 01c2 |
| Scene 16 | FF88BE110h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 01c2 0168 005a 010e 005a 0168 |
| Lower | FF8882140h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c |
| Raise | FF8882220h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 |

The only commands that get repeated when a button is held down are the Raise and Lower commands.

Radio RA Codes:

| Transmitter Button: | IR Command: | Pronto Command: |
| --- | --- | --- |
| Full Off | FF88BD120h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 005a 00b4 005a 01c2 |
| Scene 1 | FF88BD1D0h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 010e 005a 005a 0168 |
| Scene 2 | FF88BD240h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 00b4 005a 021c |
| Scene 3 | FF88BD2B0h | 0000 0069 0008 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 005a 005a 005a 00b4 0168 |
| Scene 4 | FF88BD710h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 010e 010e 005a 0168 |
| Scene 5 | FF88BD7E0h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 021c 01c2 |
| Scene 6 | FF88BD470h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 005a 010e 010e 0168 |
| Scene 7 | FF88BD480h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 005a 00b4 005a 0276 |
| Scene 8 | FF88BDD40h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 010e 005a 005a 005a 005a 021c |
| Scene 9 | FF88BDDB0h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 010e 005a 00b4 005a 00b4 0168 |
| Scene 10 | FF88BDE20h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 0168 010e 005a 01c2 |
| Scene 11 | FF88BDED0h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 0168 005a 00b4 005a 005a 0168 |
| Scene 12 | FF88BDB70h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 00b4 005a 00b4 005a 010e 0168 |
| Scene 13 | FF88BDB80h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 00b4 005a 010e 0276 |
| Scene 14 | FF88BD810h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 00b4 021c 005a 0168 |
| Scene 15 | FF88BD8E0h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 0168 005a 00b4 010e 010e 01c2 |
| Full On | FF88BE110h | 0000 0069 0006 0000 032a 010e 005a 010e 005a 005a 01c2 0168 005a 010e 005a 0168 |
| Lower | FF8882140h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c |
| Raise | FF8882220h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 |

The only commands that get repeated when a button is held down are the Raise and Lower commands.

PerSONNA and PerSONNA System:

| Transmitter Button: | IR Command: | Pronto Command: |
| --- | --- | --- |
| Lower | FF8882220h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c 032a 010e 005a 010e 005a 01c2 005a 0168 005a 005a 005a 021c |
| Raise | FF8882140h | 0000 0069 0006 0006 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 032a 010e 005a 010e 005a 01c2 005a 010e 005a 010e 005a 01c2 |
| Full Off (Low End) | FF88BD120h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 005a 00b4 005a 01c2 |
| Scene 1 (100%) | FF88BD1D0h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 010e 010e 005a 005a 0168 |
| Scene 2 (50%) | FF88BD240h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 00b4 005a 021c |
| Scene 3 (20%) | FF88BD2B0h | 0000 0069 0008 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 00b4 005a 005a 005a 005a 00b4 0168 |
| Scene 4 (10%) | FF88BD710h | 0000 0069 0007 0000 032a 010e 005a 010e 005a 005a 0168 005a 005a 005a 010e 010e 005a 0168 |

The only commands that get repeated when a button is held down are the Raise and Lower commands.

Sivoia Shades (All Shades, All Zones):

| Transmitter Button: | IR Command: | Pronto Command: |
| --- | --- | --- |
| Close | FF7D1D120h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 0112 005b 00b7 005b 00b7 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 0112 005b 00b7 005b 00b7 |
| Open | FF7D1D1D0h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 0112 0112 005b 005b 005b 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 0112 0112 005b 005b 005b |
| Preset 1 | FF7D1D240h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 00b7 005b 00b7 005b 0112 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 00b7 005b 00b7 005b 0112 |
| Preset 2 | FF7D1D2B0h | 0000 0067 0008 0008 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 00b7 005b 005b 005b 005b 00b7 005b 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 00b7 005b 005b 005b 005b 00b7 005b |
| Preset 3 | FF7D1D710h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 005b 0112 0112 005b 005b 02dc 005b 01c9 005b 005b 0112 0112 005b 005b 005b 0112 0112 005b 005b |
| Lower | FF7D22140h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 00b7 005b 0112 005b 016e 005b 005b 005b 0112 02dc 005b 01c9 005b 005b 00b7 005b 0112 005b 016e 005b 005b 005b 0112 |
| Raise | FF7D22220h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 00b7 005b 0112 005b 0112 005b 0112 005b 00b7 02dc 005b 01c9 005b 005b 00b7 005b 0112 005b 0112 005b 0112 005b 00b7 |
| Programming Mode | FF7D28280h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 00b7 005b 005b 005b 01c9 005b 005b 005b 016e 02dc 005b 01c9 005b 005b 00b7 005b 005b 005b 01c9 005b 005b 005b 016e |
| Set Limits | FF7D28720h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 00b7 005b 005b 005b 016e 0112 00b7 005b 00b7 02dc 005b 01c9 005b 005b 00b7 005b 005b 005b 016e 0112 00b7 005b 00b7 |
| Ind. Level Adj. Mode | FF7D287D0h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 00b7 005b 005b 005b 016e 01c9 005b 005b 005b 02dc 005b 01c9 005b 005b 00b7 005b 005b 005b 016e 01c9 005b 005b 005b |
| Preset Lock | FF7D28440h | 0000 0067 0007 0007 02dc 005b 01c9 005b 005b 00b7 005b 005b 005b 016e 005b 0112 005b 0112 02dc 005b 01c9 005b 005b 00b7 005b 005b 005b 016e 005b 0112 005b 0112 |

All commands are repeated.